## Slide 1
FEA Lab Project: Static & Transient Analysis
S.M.Zain ul abdeen
ME 1907
Mechanical Engineering
Instructor: Engr Affan Ahmed Khan

## Slide 2
Introduction & Material Properties
1
Project Overview
This report details Static Structural and Transient Structural analyses on a hexagon-based 3D extruded geometry.
2
Purpose
To observe the structure's response to static and time-dependent varying loads.
3
Material: ME-1900
Young's Modulus: 7000 Mpa
Poisson's Ratio: 0.28
Density: 8000 kg/m³
Material Properties (Static)

## Slide 3
Geometry Creation & Meshing
A hexagon shape was sketched on the XY-plane and extruded to a depth of 0.09 m. ANSYS automatically generated a mesh using default controls, including Hex20/Wedge elements.
Sketch (Static)
Extruded Body (Static)
Mesh Metrics (Static)

## Slide 4
Static Structural Analysis
Boundary Conditions
Fixed Support on one face.
Remote Force of 2032 N applied on opposite face (ramped).
Static Results
Equivalent (von-Mises) stress distribution obtained.
Maximum stress visible on the loaded face region.
Fixed Support (Static)
Total Deformation (Static)
Equivalent Stress (Static)
Convergence Plot (Static)

## Slide 5
Transient Structural Analysis
1
Boundary Conditions
Fixed Support on one face. Five Remote Forces (281.5 N each) on six different faces.
2
Analysis Settings
Step end time: 1.2 s. Initial time step: 0.2 s. Auto time stepping: ON. Loads follow a triangular ramp-up/ramp-down.
3
Transient Results
Time-based equivalent stress distribution. Max stress: 2.4614e2 Pa at t ≈ 1 s, then decreases.
Fixed Support (Transient)
Deformation vs Time (Transient)
Stress-Time Response (Transient)
Strain Energy (Transient)

## Slide 6
Observations & Conclusion
Stress Concentrations
Consistent with applied load faces in both analyses.
Dynamic Response
Transient analysis showed dynamic response to varying loads.
Mesh Quality
Acceptable for student version settings.
Successful Analyses
Both static and transient analyses were successfully performed.
The object behaves predictably under both constant and time-varying loads.